## Slide 1: Energy efficient UDN design using reinforcement learning
BongSang Kim
Jaehyun Lee
DGIST
tph02361@dgist.ac.kr
dlwogus4066@dgist.ac.kr
25/July/2019
Summer Internship
Final Presentation

## Slide 2: Outline
Overview
  Background
  Objectives
UDN design
  System Model
  RL setup
  Results
Future Study
  Plan

## Slide 3
Overview
Part 1

## Slide 4: Background : Ultra Dense Network(UDN)
Ultra Dense Network(UDN)
  Dense and massive deployment of BSs
  Has higher data rates and enhanced coverage
  BS to UE ratio is higher than traditional cellular network
  Due to the densification of BSs, BS have LoS/NLoS path
  Turning off surplus BS can increase data rates considering interferences

## Slide 5: Background : Reinforcement Learning(RL)
Reinforcement learning
  Agent takes actions in an environment to maximize total reward.
    Agent receives state from the environment
    Agent takes an action at the state
    Environment goes to a next state
    Agent receives reward from the environment

## Slide 6: Background : DQN algorithm
Deep Q Network(DQN)
  Update action-value function
  Choose deep neural network as non-linear function approximator
  of action-value(Q) function
  Value based method
Notes: 강화학습에서 agent는 environment를 MDP를 통해서 이해를 하는데 table 형태로 학습을 모든 state에 대한 action-value function의 값을 저장하고 update시켜나가는 식으로 하면 학습이 상당 히 느려집니다. 따라서 approximation을 하게되고 그 approximation방법 중에서 nonlinear function approximator로 deep neural network가 있습니다. 따라서 action-value function(qvalue)를 approximate하는 방법으로 deep neural network를 택한 reinforcement learning방법이 Deep Reinforcement Learning(deepRL)입니다. 또한 action value function뿐만 아니라 policy 자체를 approximate할 수도 있는데 그 approximator로 DNN을 사용해도 DeepRL이 됩니다.

## Slide 7: Objectives
Energy efficient UDN environment design
  BSs consume energy in proportion to the # of active BSs
  Data rates increase as active BSs increase
  However, the densification of BSs in UDN cause stronger interference
    UDN efficiency decreases
Find optimal BS on/off strategy in UDN using DQN algorithm

## Slide 8
UDN design
Part 2

## Slide 9: UDN Environment Modeling
Parameters
  Control Area =
  Users = 16
  BS number = 6
  Interference BS number =64
  Interference BS state = Random on/off in each state
  BS location is PPP()
  First user position = random position in control area
  User location change = walking model
  User-BS association rule: nearest BS association
  Bandwidth = 10
  Path loss exponential factor = -4

## Slide 10: UDN Environment Modeling
Channel model
  Path loss model
  User received signal power =
  User received interference power =
  SIR =
  Data rate at user k =

## Slide 11: UDN Environment Modeling

## Slide 12: RL setup
Model uses gym and pytorch library
Use DQN algorithm
  State: Matrix of UE position [UE x position, UE y position]
  Action: Changing each BS on/off state, discrete
    Action uses Binary-coded decimal(BCD)
      Can reduce memory usage & easy to handle than matrix type.
      Action space=[0, 0, 0, …, 0], … [1, 1, 1, …, 1]
      Action space=range(64)
  Reward:
Notes: BCD는 이진화 십진법

## Slide 13: RL setup
-greedy
  decays linearly from 0.99 to 0 based on # of episodes
Use Buffer to make mini batch
  Buffer size limit = 50000, FIFO
  Batch size= 1024
Use TD(0), (=0.99)
Use q-target network
  Could stabilize target value
Notes: Epsilon greedy에서 엡실론 값은 0.99-0.1*(episode_number)/700을 따른다. 근데 이건 에피소드 개수따라 달라져야 해서 전체에피소드의 70%는 nonzero epsilo값이고, 30%는 zero값인 epsilon으로 학습
엡실론 decay를 사용하면 학습 초기에 exploration을 크게 늘릴 수 있고, overfitting을 방지할 수 있다.
하지만 TD에서는 실제 보상과 다음 step에 대한 미래추정가치를 사용해서 학습을 하게 됩니다.
이때 사용하는 보상과 value function의 합을 TD target이라고합니다.
그리고 이 TD target과 실제 V(S)와의 차이를 TD error 라고 하고 델타라고 표현을 합니다.
https://computer-nerd.tistory.com/46

## Slide 14: RL setup
Use DQN algorithm
Neural network design
  Use fully connected network
  # of input nodes is dimension of state, which is
  # of hidden layer nodes is 100 each, has 2 hidden layer
  # of output nodes is dimension of possible actions, which is
Q
Hidden layer 2
Hidden layer 1
Input
Fully Connected
Fully Connected, ReLu
Fully Connected, ReLu
64(=)
100
32
100

## Slide 15: RL setup
4 python module
  main.py: DQN algorithm code
  UDN_env.py: gym environment
  BSppp.py: create BSposition.csv
    Information of BS position
  InterferenceBSppp.py: create InterferenceBSposition.csv
    Information of interference BS position

## Slide 16
RL setup-Structure-main.py
Class : Qnet(nn.Module)
__init__
forward
sample_action
train
main
Construct neural network
Select activation function - ReLu
-greedy
Buffer stores
Update q function – use mini batch and q-target network
Import gym_UDN, initialize parameters, run DQN
Class : Replay Buffer

## Slide 17
RL setup-Structure-UDN_env.py
Class : UDNEnv
__init__
take_action
step
reset
association
usermovedistance
Interference_User_I
Initialize parameters, BS/UE position
Calculate BS distance, Energy consumption, SIR, Reward
Reset parameters(state, UE position)
Associate BS-UE by association rule
Move UE at some distance from current location
Return the state according to action
Return interference of each UE

## Slide 18
Simulation Result terminate at 10000 episode

## Slide 19
Simulation Result terminate at 20000 episode

## Slide 20
Simulation Result terminate at 50000 episode

## Slide 21
Simulation Result terminate at 10000 episode

## Slide 22
Simulation Result terminate at 20000 episode

## Slide 23
Simulation Result terminate at 50000 episode

## Slide 24
Future Study
Part 3

## Slide 25: Plan
Environment model
  Consider LoS, BS Elevation, backhaul, Interference
  Update association rule
  Update SNR to SINR
RL model
  Re-design reward
  Re-design terminal condition
  Apply other algorithms
    Actor – Critic
    MCTS

## Slide 26: Thank you
Any Questions?
Email : tph02361@dgist.ac.kr, dlwogus4066@dgist.ac.kr