## Slide 1: Impact of Elevated Base Stations on the Ultra-Dense Networks
BongSang Kim
School of Undergraduate studies
Daegu Gyeongbuk Institute of Science and Technology (DGIST)
tph02361@dgist.ac.kr
April. 25, 2019
UGRP
Hewon Cho, Chenxi Liu, Jemin Lee , Taegyun Noh, and Tony Q. S. Quek

## Slide 2: Keywords
Elevated BSs
LoS(Line of Sight)/NLoS
Stochastic geometry
Coverage probability

## Slide 3: UDN Characteristics
-The distance between BS and UE is small
The height of BSs cannot be ignored
The possibilities of having LoS propagation increases.
Notes: 모바일 사용자의 트래픽 수요가 폭등하면서 5G에서는 주요 후보 기술 분야로 기지국 간 거리가 매우 가까운 초고밀도 네트워크가 있다.
UDN에서 상대적으로 많은 기지국들을 통해서 높은 주파수 효율과 데이터 전송 속도를 보장할 수 있다.

## Slide 4: Former studies models
Assumption: the probability of LoS propagations decreases as the antenna height of BSs increases -unlikely to be valid in practice
- BSs with a higher height are more likely to establish the LoS path towards the UEs.
Assumption: equal height for all BSs-not realistic.
heights of buildings should be different and random
Notes: Ideal Backhaul: 2.5 이하의 지연과 10Gbps 이상의 capacity를 갖는 backhaul
Non-ideal Backhaul: 5~30 msec (혹은 그 이상)의 지연을 갖는 backhaul
Ideal Backhaul: 2.5𝜇𝑠𝑒𝑐 이하의 지연과 10Gbps 이상의 capacity를 갖는 backhaul
Non-ideal Backhaul: 5~30 msec (혹은 그 이상)의 지연을 갖는 backhaul

## Slide 5: System Model
Single-antenna BSs and single-antenna Ues are randomly distributed.
Modeled as PPPs(Poisson point processes) respectively( and
each BS has at least one UE associated in its coverage for simplicity

## Slide 6: System Model-Network Description
All BSs have their antennas at the height
All UEs are on the ground
Each BS supports one UE using time and frequency with the same transmission power.
each BS has a LoS/NLoS path to associated UE with probability

## Slide 7: System Model-Network Description
Consider both fading and path loss
LoS/NLoS propagation experiences Nakagami-m fading
*LoS: Rician fading
*NLoS: Rayleigh fading
Path loss exponent
Notes: NLoS transmission: is independent with the BS density when is large enough.
  Increase in interference and signal power cancel each other
NLoS transmission: ASE increases linearly with the BS density .
  is invariable with respect to
NLoS transmission: 𝑃_𝑐𝑜𝑣 is independent with the BS density 𝜆 when 𝜆 is large enough.
  Increase in interference and signal power cancel each other
NLoS transmission: ASE increases linearly with the BS density 𝜆.
  𝑃_𝑐𝑜𝑣 is invariable with respect to 𝜆

## Slide 8: BS Association Rule
the path loss exponents are different for LoS and NLoS propagations
the signal strength of the nearest BS is not always the strongest one
cf) conventional model : the signal strength of the nearest BS is the strongest one
Consider BS with average strongest received power.

## Slide 9: BS Association Rule
Conventional PDF of the distance between UE and BS canoot be applied to the system.
Should be consider LoS/NLoS propagation respectively.

## Slide 10: BS Association Rule
The approximated PDFs of
LOS
NLOS
: tunable value determined by the BS height
Notes: Serving BS가 BS height 보다 더 가까이 있을 수는 없기 때문에 Signal power는 제한되지만, BS 밀도가 높아지면서 Interfering BS의 개수가 많아져 Interference power는 더 높아져 결과적으로 coverage probability와 ASE는 BS높이가 높아짐에 따라 감소하게된다.
𝜆가 0에 가까워진다는 것은 BS 밀도가 아주 작아져서 BS 사이 거리가 아주 멀다는 것을 뜻하고, 따라서 BS의 높이는 무시할 수 있다.

## Slide 11: Signal-to-Interference Radio
SIR at the typical UE located at the origin
: channel fading(LoS: , NLoS:
: horizontal distance between UE and BS
: pathloss exponent
: total interference power received from BSs in

## Slide 12: Coverage Probability analysis
The coverage probability of the system is

## Slide 13: Remark: Coverage Probability Analysis
Coverage Probability
  The coverage probability when the main link transmitter is in j-tier under channel c is selected with distance d
    : SINR threshold
    f is SINR when the main link transmitter is in the j-tier under channel c with distance d

## Slide 14: Numerical Results

## Slide 15: Numerical Results

## Slide 16: Questions?
Thank you