## Slide 1: UDN Overview - 2019 UGRP-
Jemin Lee
Information and Communication Engineering
Daegu Gyeongbuk Institute of Science and Technology (DGIST)
jmnlee@dgist.ac.kr
Feb. 21, 2019

## Slide 2: Outline
Part 1 - Ultra-Dense Network (UDN) Overview
Part 2 – UDN Modeling
Part 3 – UDN Performance

## Slide 3
Part 1
UDN Overview

## Slide 4: Ultra-Dense Network (UDN)
Dense and massive deployments of small-cell BSs
Core element to realize the vision of 5G
Higher data rates and enhanced coverage
Notes: 모바일 사용자의 트래픽 수요가 폭등하면서 5G에서는 주요 후보 기술 분야로 기지국 간 거리가 매우 가까운 초고밀도 네트워크가 있다.
UDN에서 상대적으로 많은 기지국들을 통해서 높은 주파수 효율과 데이터 전송 속도를 보장할 수 있다.

## Slide 5: Ultra-Dense Network(UDN)
ITEM | UDN | Traditional cellular network
Deployment Scenarios | Indoor, Hotspot | Wide coverage
AP density | More than 1000/km2 | 3-5/km2
AP Coverage | Around 10m | Several hundred meters and more
AP types | Small-Cell, Pico, Femto, UE relay, Relay | Macro/Micro BS
AP Backhaul | Ideal/Non-ideal, Wired/Wireless | Ideal, Wired
User Density | High | Low/Medium
User Mobility | Low mobility | High mobility
Traffic density | High | Low/Medium
Deployment | Heterogeneous, irregular | Single layer, regular cell
System Bandwidth | Hundreds of MHz | Tens of MHz
Spectrum | >3GHz (up to mm Wave) | <3GHz
[Sha:17] Chen, Shanzhi, et al. "Ultra-Dense Network Architecture and Technologies for 5G." 5G Mobile Communications. Springer International Publishing, 2017. 403-429.
Comparison between UDN and the traditional cellular network
Notes: Ideal Backhaul: 2.5 이하의 지연과 10Gbps 이상의 capacity를 갖는 backhaul
Non-ideal Backhaul: 5~30 msec (혹은 그 이상)의 지연을 갖는 backhaul
Ideal Backhaul: 2.5𝜇𝑠𝑒𝑐 이하의 지연과 10Gbps 이상의 capacity를 갖는 backhaul
Non-ideal Backhaul: 5~30 msec (혹은 그 이상)의 지연을 갖는 backhaul

## Slide 6: Why are Dense SCNs Different?
Dense Small Cell Networks (SCNs) are different:
  Stronger interference due to the transition from NLoS to LoS
  Capped signal due to the BS-to-UE antenna height difference
  BS diversity gain due to a surplus of base stations than users
  UE diversity loss due to a small number of UEs in each cell
D. Lopez-Perez, M. Ding, H. Claussen, A. Jafari, “Towards 1Gbps/UE: Understanding Ultra Dense Small Cell Deployments,” IEEE Comm. Surveys & Tutorial, 2015

## Slide 7: Transition from NLoS to LoS
Probabilistic LoS and NLoS transmissions
UE may be associated with a BS having a LoS path to the UE
Ding, Ming, et al. "Performance impact of LoS and NLoS transmissions in dense cellular networks." IEEE Transactions on Wireless Communications 15.3 (2016): 2365-2380.
Serving BS
Interfering BSs
Serving BS
Interfering BSs
UDN
Due to the densification of BSs in UDN, both serving BS and interfering BSs may have a LoS path to the UE

## Slide 8: Transition from NLoS to LoS
Probabilistic LoS/NLoS transmissions:
Ding, Ming, et al. "Performance impact of LoS and NLoS transmissions in dense cellular networks." IEEE Transactions on Wireless Communications 15.3 (2016): 2365-2380.
Stronger Interference due to the Transition from NLoS to LoS
ASE decreases as increases in some range.
  Due to the quick decrease of the
decreases as increases when the network is dense enough.
  Due to the transition of a large number of interference paths from NLoS to LoS
Notes: NLoS transmission: is independent with the BS density when is large enough.
  Increase in interference and signal power cancel each other
NLoS transmission: ASE increases linearly with the BS density .
  is invariable with respect to
NLoS transmission: 𝑃_𝑐𝑜𝑣 is independent with the BS density 𝜆 when 𝜆 is large enough.
  Increase in interference and signal power cancel each other
NLoS transmission: ASE increases linearly with the BS density 𝜆.
  𝑃_𝑐𝑜𝑣 is invariable with respect to 𝜆

## Slide 9: BS Antenna Heights
BS-to-UE antenna height difference is not negligible
  UE cannot be closer than to its serving BS
  A cap on the signal power
If is larger than zero, then the ASE performance will continuously decrease with network densification for UD SCNs.
Ding, Ming, and David López Pérez. "Please lower small cell antenna heights in 5G." Global Communications Conference (GLOBECOM), 2016 IEEE. IEEE, 2016.

## Slide 10: BS Antenna Heights
Ding, Ming, and David López Pérez. "Please lower small cell antenna heights in 5G." Global Communications Conference (GLOBECOM), 2016 IEEE. IEEE, 2016.
Weaker Signal due to the BS-to-UE Antenna Height Difference
: ASE increases linearly
3GPP case: ASE crawls
  Transition from NLoS to LoS
Non-zero : ASE crashes
  Sever performance loss in UD SCNs
  A cap imposed on the signal-link distance and signal power
: BS density does not matter
3GPP case: converges to a constant
  Interference and signal powers are LoS dominated
Non-zero : converges to 0
  A cap on the signal power and growth of interference power

## Slide 11: Elevated Base Stations
BS Height
Atzeni, Italo, Jesús Arnau, and Marios Kountouris. "Downlink cellular network analysis with LOS/NLOS propagation and elevated base stations." arXiv preprint arXiv:1703.01279 (2017).
Effect of BS height on the network performance
Lower interfering signal power
Lower received signal power
(Bounded pathloss)
    Detrimental Effect of BS Height
Network Performance
Notes: Serving BS가 BS height 보다 더 가까이 있을 수는 없기 때문에 Signal power는 제한되지만, BS 밀도가 높아지면서 Interfering BS의 개수가 많아져 Interference power는 더 높아져 결과적으로 coverage probability와 ASE는 BS높이가 높아짐에 따라 감소하게된다.
𝜆가 0에 가까워진다는 것은 BS 밀도가 아주 작아져서 BS 사이 거리가 아주 멀다는 것을 뜻하고, 따라서 BS의 높이는 무시할 수 있다.

## Slide 12: Elevated Base Stations
Cellular Network with Elevated Base Stations (not a UDN)
System Model
  Bounded pathloss model
    BS cannot be closer than the height of BS,
  NLoS transmission only
    Rayleigh fading, same pathloss exponent for NLoS and LoS
Atzeni, Italo, Jesús Arnau, and Marios Kountouris. "Downlink cellular network analysis with LOS/NLOS propagation and elevated base stations." arXiv preprint arXiv:1703.01279 (2017).

## Slide 13
Part 2
UDN Modeling

## Slide 14: Things to Think for UDN Modeling (1/2)
Base station distribution
  Density?
  How to distribute?
Mobile user distribution
  Density?
  How to distribute?
BS association
  BS with average strongest received power
  BS with instantaneous strongest received power

## Slide 15: Things to Think for UDN Modeling (2/2)
Channel Modeling
  LoS probability?
  Channel fading?
Interference Modeling
  Co-channel interference from all BSs (Downlink case) or parts of BSs?

## Slide 16: Base station distribution
Conventional Cell – Hexagonal Cells

## Slide 17: Base station distribution
Poisson distributed base stations?

## Slide 18: Base station distribution
확률 기하(stochastic geometry)
  공간상 무작위의 패턴을 분석하는 학문
  고밀집 네트워크 연구에서 최적의 이론적 분석 방법
  실제 기지국 분포 vs. PPP(Poisson Point Process) 기지국 분포[1]
    실제 미국의 LTE 기지국 분포 (40km x 40 km)
    실제 기지국과 PPP 기지국 분포가 상당히 유사함
<(좌) 실제 LTE 기지국 분포, (우) 동일 밀도를 갖는 PPP 기지국 분포 >
<기지국 분포 방식에 따른 커버리지 확률 비교>

## Slide 19: Base station distribution – PPP
Definition of Poisson Point Process (PPP)
  Consider the count function for a point process
  A Poisson point process (PPP) on is a random countable subset of such that
  1) for any disjoint measurable subsets of ,
  the random variables are independent
  2) has the Poisson distribution with mean
  where

## Slide 20: Base station distribution – PPP
PPP is perhaps the most well-studied point process
  No dependence between node locations
  Random number of nodes
  Can be defined on the entire plan
An Example of PPP

## Slide 21: Base station distribution – PPP
How to simulate a PPP of density on A = [-L,L]2 ?
  1) The number of points in the set A is a Poisson random variable with mean
  2) Conditioned on the number of points, the points are uniformly distributed as a BPP on A
Can generate one realization of a PPP
Need to repeat to obtain average behavior

## Slide 22: BS Association Rule
BS (or AP) Association
  “Biasing” in Association
    To push users off from heavily loaded macrocell to lightly loaded small cell
    Fixed or adaptive or random biasing
  Optimal Association: Massive Combinatorial Optimization Problem
    SINR for every user to every BS
    Instantaneous load at each BS
    Choices of other users in the network
[And14] J. G. Andrews et al., “An Overview of Load Balancing in HetNets: Old Myths and Open Problems”, IEEE Wireless Commun., 2014.
Instantaneous max SINR Association
(Biased) Average Max Received Power Association
* [And14]
Notes: to make a user associate with lower sINR than the maceocell

## Slide 23: BS Association Rule
“Average” Strongest BS Association Rule
  Due to the different pathloss exponent for LoS and NLoS propagation, the nearest BS may not transmit the strongest power
  Different distribution of the main link distance depending on whether the serving BS forms LoS or NLoS Propagation

## Slide 24: Channel Modeling
LoS Link? Or NLoS Link?

## Slide 25: Channel Modeling - LoS Probability
Height of the ray at the obstruction point,
Probability that a LoS ray exists
Propagation data and prediction methods required for the design of terrestrial broadband radio access systems operating in a frequency range from 3 to 60 GHz, ITU-R, p.1410-5, Feb, 2012.
Notes: 𝑏_𝑟: number of buildings crossed

## Slide 26: Channel Modeling - LoS Probability
Three Environment Parameters
  : the ratio of land area covered by buildings to total land area
  : the mean number of buildings per unit area [buildings/km2]
  : a variable determining the building height distribution
Propagation data and prediction methods required for the design of terrestrial broadband radio access systems operating in a frequency range from 3 to 60 GHz, ITU-R, p.1410-5, Feb, 2012.
Expected number of buildings passed per km:
Number of buildings in :
Notes: : number of buildings crossed
𝑏_𝑟: number of buildings crossed

## Slide 27: Channel Modeling - LoS Probability
Approximated LoS Probability
  Parameters and are directly linked to the environment variables , , and
  Obtained by Surface fitting:
Al-Hourani, Akram, Sithamparanathan Kandeepan, and Simon Lardner. "Optimal LAP altitude for maximum coverage." IEEE Wireless Communications Letters 3.6 (2014): 569-572.
Similar to Sigmoid function

## Slide 28: LoS Probability
Increasing LoS Probability with BS Height
LoS Probability for 3GPP LoS/NLoS model
[Kat:16] Haneda, Katsuyuki et al. “5G 3GPP-like Channel Models for Outdoor Urban Microcellular and Macrocellular Environments.” VTC Spring (2016).
[Akr:14] Al-Hourani, Akram, Sithamparanathan Kandeepan, and Simon Lardner. "Optimal LAP altitude for maximum coverage." IEEE Wireless Communications Letters 3.6 (2014): 569-572.
LoS Probability for 3GPP LoS/NloS Model[Kat:16]
3D-based LoS Probability[Akr:14]
  Decreases with BS Height
  Increases with BS Height

## Slide 29: Interference
Frequency Allocation per Frequency Band

## Slide 30: Interference
Co-Channel Interference

## Slide 31: Interference
Co-Channel Interference and Frequency Reuse

## Slide 32: Interference
Exercise: Assume the transmitting nodes from a stationary PPP of intensity in . All nodes transmit at unit power, and the pathloss is . The interference at origin is
  where is the PPP of the distance
  Due to the stationarity of the PPP, the distribution of the interference is the same everywhere.

## Slide 33: Interference
Frequency allocation and planning is necessary for the coverage
  As it affects the interference
For frequency bands, we can simply consider the random allocation of bands
  Corresponds to the thinning of a PPP
    So, the density of BSs using
    the frequency band m is
We first consider the nearest BS
to the MS at the origin
  Distance distribution of main link
  Interferer density

## Slide 34
Part 3
UDN Performance

## Slide 35: System Model
Channel Modeling
  Pathloss exponent
    LoS: 2.5, NLoS: 4
  Nakagami-m fading for LoS and NLoS channels
    Channel gain of (C),
    Shape parameter
      then, Exponential Distribution for NLoS channel
      Bigger results in smaller variance LoS channel
Received Power
  Received power of the user
    : Link distance
    : Representing whether channel is LoS/NLoS

## Slide 36: System Model
Association Rule
  Strongest average received power based association
  and are coordinates of the main link transmitter and the receiver
  is pathloss of the corresponding transmitter
  Both LoS and NLoS channel are considered
Interference
  The interference from the k-tier under channel environment
  Sum of interference and noise
    : Noise

## Slide 37: Coverage Probability Analysis
Coverage Probability
  The coverage probability when the main link transmitter is in j-tier under channel c is selected with distance d
    : SINR threshold
    f is SINR when the main link transmitter is in the j-tier under channel c with distance d

## Slide 38: Area Spectral Efficiency
Area Spectral Efficiency (ASE)
  The ASE [bps/Hz/] of j-tier network
    : Target SINR threshold of the STP
  The ASE of the UDN

## Slide 39
Information Security and Communications (ISC) Lab.
Any Questions?
THANK YOU
Email : jmnlee@digist.ac.kr