## Slide 1: Impact of Elevated Base Stations on the Ultra-Dense Networks
BongSang Kim
25/April/2019
UGRP
Hewon Cho, Chenxi Liu, Jemin Lee , Taegyun Noh, and Tony Q. S. Quek
Notes: 표지

## Slide 2: Keywords
Elevated BSs
LoS(Line of Sight)/NLoS
Stochastic geometry
Coverage probability
Notes: 키워드

## Slide 3: UDN Characteristics
-The distance between BS and UE is small
The height of BSs cannot be ignored
The possibilities of having LoS propagation increases.
Notes: UDN 특성
잠깐 UDN에 대해 간략히 복습하자면
@#@#@#@#@_@

## Slide 4: Former studies models
Assumption: the probability of LoS propagations decreases as the antenna height of BSs increases -unlikely to be valid in practice
- BSs with a higher height are more likely to establish the LoS path towards the UEs.
Assumption: equal height for all BSs-not realistic.
heights of buildings should be different and random
Notes: Former studies 한계, 문제점?

## Slide 5: System Model
Single-antenna BSs and single-antenna Ues are randomly distributed.
Modeled as PPPs(Poisson point processes) respectively( and
each BS has at least one UE associated in its coverage for simplicity

## Slide 6: System Model-Network Description
All BSs have their antennas at the height
All UEs are on the ground
Each BS supports one UE using time and frequency with the same transmission power.
each BS has a LoS/NLoS path to associated UE with probability

## Slide 7: System Model-Network Description
Consider both fading and path loss
LoS/NLoS propagation experiences Nakagami-m fading
*LoS: Rician fading
*NLoS: Rayleigh fading
Path loss exponent

## Slide 8: BS Association Rule
the path loss exponents are different for LoS and NLoS propagations
the signal strength of the nearest BS is not always the strongest one
cf) conventional model : the signal strength of the nearest BS is the strongest one
Consider BS with average strongest received power.

## Slide 9: BS Association Rule
Conventional PDF of the distance between UE and BS canoot be applied to the system.
Should be consider LoS/NLoS propagation respectively.

## Slide 10: BS Association Rule
The approximated PDFs of
LOS
NLOS
: tunable value determined by the BS height

## Slide 11: Signal-to-Interference Radio
SIR at the typical UE located at the origin
: channel fading(LoS: , NLoS:
: horizontal distance between UE and BS
: pathloss exponent
: total interference power received from BSs in

## Slide 12: Coverage Probability analysis
The coverage probability of the system is

## Slide 14: Numerical Results

## Slide 15: Numerical Results

## Slide 16: Questions?
Thank you