## Slide 1: Energy efficient UDN design using reinforcement learning
DGIST
BongSang Kim
JaeHyun Lee
19/July/2019
UGRP Meeting

## Slide 2: Progress
Design Env code
Design RL code – MCTS
  Remodel based on sample library
    Most of MCTS libraries are for sequential game
     We decided to mcts.py module instead of using MCTS library
Make 2 module
  main.py: UDNEnv(environment code)+MCTS(RL code)
  ppp.py: BSposition.csv(information of BS position) create

## Slide 3: System Model
Environment model
  16-users and 10-BSs are deployed in the area
    BS location is PPP
    User location is uniform distribution which changes every step
    전원 off 된 BS와 user까지의 거리를 infinity로 하여 association을 막음
MCTS model
  Utilize MCTS library on Github
    Most of MCTS libraries are for sequential game
  We decided to edit the library for our environment model

## Slide 4: System Model
MCTS design
  Reward: SIR + Energy consumption, [ (NLoS) ]
  : Distance between User and BS matrix
    [BS, UE is location matrix of BS and User]
  Node: initialize with for every
  Initial policy:
  Constraint: one action, one BS condition change 
  one action, every BS condition could change
  Optimize policy – update by backpropagation

## Slide 5: System Model
Environment model based on gym environment & tensorflow lib.
  State: Matrix of BS on/off [discrete, BS on, 𝑖=1, 2, …,n ]
    Use matrix for describing entire state
  Action: Matrix of change BS on/off state [discrete]
    action change BSs state at the same time
    Previous : BS state changed by action in order
      is more significant than in this case ,
      as has priority in backpropagation
      We suppose each BS identical, so this model has been discarded.
  Reward: (Sum of each SNR / Sum of Energy Consumption)
  User-BS association rule: nearest BS association

## Slide 6: System Model
Make 2 python module
  main.py: UDNEnv(environment code)+MCTS(RL code)
  ppp.py: create BSposition.csv(information of BS position)

## Slide 7: System Model Structure
Class : UDNEnv
  __init__ : Initialize parameters, BS position, depthLimit
  Step : calculate Bsdistance/EnergyConsumption/SNR/reward
      Initialize UE position(at every iteration)
      Update State / Reward
  Association : associate BS/UE by association rule
  Binary convert : convert integer number to binary action
  isTerminal : decide whether the state is terminal or not
        Terminate when reach at
        Return True/False
  getPossibleAction : return list of every possibleaction
  takeAction(action) : return the state according to action
  getReward(action) : return the reward of specific state

## Slide 8: System Model Structure
Class : mcts
  __init__ : initialize parameters
  search : search Tree until iterationlimit
  executeRound : update node/reward, do backpropagate
  selectNode : decide next node
  expand : expand new node
  Backpropagate : backpropagate the tree
  getBestChild : find possible bestNodes
  getAction : return action of bestnode

## Slide 9: Future plan
Program RL code by Tensorflow Library
Apply UDN at our Environment
  Consider LoS, NLoS, Interference
  Set BS density for UDN
  Consider all BS state change concurrently
  Update reward
    consider Energy Consumption
    SNR
    Terminal condition - reach at Terminal Node or SNR < threshold
Update RL code for programmed env code
Sample another environment to check policy is overfit or not

## Slide 10: Thank you
Any Questions?